Esplora Pins
Switch 4: M0011
Switch 3: M0010
Switch 1: M0000
Switch 2: M0001
Joystick
X-axis: M1011
Y-axis: M1100
Press: M1010
Temperature: M0110
Accelerometer
X-axis: A5
Y-axis: A11
Z-axis: A6
Slider: M0100
Microphone: M0111
LED: D13
RGB LED
Red: D5
Blue: D9
Green: D10
Light Sensor: M0101
Buzzer: D6
The following provides all the pins that connect to the onboard sensors and what pins the headers provide. For a key to pin names please see the last page.

Right Pin Header
1. 5V
2. D14
3. D15
4. D16
5. D7
6. D8
7. D0 / RX
8. D1 / TX
9. 5V
10. GND

5V
D11
GND

5V
D3
GND

5V
M1000
GND

5V
M1001
GND

Key

Dxx	Digital pin xx.
e.g. D12 is digital pin 12

Axx	Analog pin xx
e.g. A5 is analog pin 5

Mxxxx	Multiplexer channel xxxx
Because there is too many analog pins for the Esplora to handle naturally	we use the in built multiplexer. The multiplexer allows us to use the	Esplora's 5 analog pins A0 to A4, to return 13 different analog sensors.
This works by setting each of the pins A0 to A3 to either high or low and	depending on this combination the multiplexer gives us one of our	sensor values on pin A4.
So each x in Mxxxx above can be either 0 or 1. If the first x is 1 we set	A3 to high otherwise we set it to low. If the second x is 1 we set A2 to	high otherwise we set it to low. If the third x is 1 we set A1 to high	otherwise we set it to low. If the fourth x is 1 we set A0 to high otherwise	we set it to low. Then we read the value at A5 to get the sensor value.
e.g. M1010 would mean we set A3 to high, A2 to low, A1 to high and A0	to low. Then we read the value at A5 to get the sensor value.

5V	Pin provides 5 volts

GND	The ground pin